## Slide 1: P&S Modern SSDs Cutting-Edge Research in SSDs
Dr. Jisung Park
Prof. Onur Mutlu
ETH Zürich
Fall 2022
04 January 2023

## Slide 2: Pipelined & Adaptive Read-Retry
The 26th International Conference on Architectural Support
for Programming Languages and Operating Systems
(ASPLOS’21)

## Slide 3: Problem: Long, Non-Deterministic Latency
NAND Flash-Based SSD
Read request (4 KiB)
Requested data
Expected latency: 100 µs
Actual latency: > 1 ms
Degrades the quality of service
of read-intensive, latency-sensitive applications

## Slide 4: Problem: Long, Non-Deterministic Latency
Requested data
Expected latency: 100 µs
Actual latency: > 1 ms
Flash-Translation Layer (FTL):
SSD Firmware
Flash Controller#1
NAND
Flash
Chip#1
NAND
Flash
Chip#2
⋯
⋯
Read Chip#2
Read CMD
NAND Flash-Based SSD
Retries
Internal Read-Retry Operations
Read request (4 KiB)

## Slide 5: Errors in NAND Flash Memory
NAND flash memory stores data by using cells’ VTH levels
Number of Cells
1
Erased State
0
Programmed
State
Cell’s VTH Level
Read–Reference Voltage VREF
<VTH Distribution of an SLC Page>
VREF
1
0
VREF
1
0

## Slide 6: Errors in NAND Flash Memory
Various sources shift and widen programmed VTH states
  Retention loss, program interference, read disturbance, etc.
Number of Cells
1
Erased State
0
Programmed
State
Cell’s VTH Level
Read–Reference Voltage VREF
<VTH Distribution of an SLC Page>
Retention loss
Interference
Errors

## Slide 7: Error-Correcting Codes (ECC)
Store redundant information (ECC parity)
  To detect and correct row bit errors
NAND Flash Chip
Page 0
Page 1
Page 2
Page 3
…
ECC Parity
Flash Controller
ECC Engine
Request Handler
NAND
command
Data
transfer
Read Page 0

## Slide 8: Error-Correcting Codes (ECC)
Store redundant information (ECC parity)
  To detect and correct row bit errors
NAND Flash Chip
Page 0
Page 1
Page 2
Page 3
…
ECC Parity
Flash Controller
ECC Engine
Request Handler
NAND
command
Data
transfer
Corrected data

## Slide 9: Errors in Modern NAND Flash Memory
High row bit-error rates (RBER) in MLC NAND flash memory
  Narrow margin b/w adjacent VTH states
# of cells
Erased (E)
0
Programmed
1
VREF
VTH
<VTH Distribution of an SLC Page>
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
VREF0
VREF1
VREF2
VREF3
VREF4
VREF5
VREF6
VTH Margin
VTH
<VTH Distribution of a TLC Page>

## Slide 10: Errors in Modern NAND Flash Memory
High row bit-error rates (RBER) in MLC NAND flash memory
  Narrow margin b/w adjacent VTH states
# of cells
111
E
110
P1
100
P2
000
P3
010
P4
011
P5
001
P6
101
P7
MSB
LSB
CSB
VREF0
VREF1
VREF2
VREF3
VREF4
VREF5
VREF6
VTH Margin
VTH
<VTH Distribution of a TLC Page>
Strong ECC: Corrects ~80 bit errors per 1-KiB data
Not Scalable: Area, power, latency, …
What if RBER > ECC Capability?

## Slide 11: Read-Retry Operation
Reads the page again with adjusted VREF values
…
Number of Cells
Px State
P(x-1) State
…
P(x+1) State
V
REF(x-1)
V
REFx
Cell’s VTH Level
V
REF(x-2)
V
REF(x+1)
Erroneous cells

## Slide 12: Read-Retry Operation
Reads the page again with adjusted VREF values
…
Number of Cells
Px State
P(x-1) State
…
P(x+1) State
V
REF(x-1)
V
REFx
V
REF(x-2)
V
REF(x+1)
V’
REF(x-2)
V’
REF(x-1)
V’
REFx
V’
REF(x+1)
Erroneous cells
Read-retry: Adjusting VREF values
Cell’s VTH Level
Read using properly-adjusted VREF values
Decreases # of raw bit errors
to be lower than the ECC capability

## Slide 13: Read-Retry: Performance Overhead
NERR = 32
< ECC capability CECC = 72
READ A
tREAD
tR: Page sensing
tDMA: Data transfer
tECC: ECC decoding

## Slide 14: Read-Retry: Performance Overhead
tR
tECC
READ A
NERR = 232
tREAD
RR1
NERR = 173
RR(N – 1)
RRN
⋯
⋯
tRETRY
NERR = 87
NERR = 23
= N×(tR+tDMA+tECC)
NERR = 118
RR2
> ECC capability CECC = 72
tDMA
Read-retry increases the read latency
almost linearly with the number of retry steps

## Slide 15: P&AR2: Outline
Read-Retry in Modern NAND Flash-Based SSDs
PR2: Pipelined Read-Retry
AR2: Adaptive Read-Retry
Evaluation Results

## Slide 16: Pipelined Read-Retry (PR2): Key Idea
tR
tECC
READ A
NERR = 232
tREAD
RR1
NERR = 173
RR(N – 1)
RRN
⋯
⋯
tRETRY
NERR = 87
NERR = 23
= N×(tR+tDMA+tECC)
NERR = 118
RR2
> ECC capability CECC = 72
tDMA
In common cases, multiple (up to 25) retry steps occur

## Slide 17: Pipelined Read-Retry (PR2): Key Idea
tR
tECC
READ A
NERR = 232
tREAD
RR1
NERR = 173
RR(N – 1)
RRN
⋯
⋯
tRETRY
NERR = 87
NERR = 23
= N×(tR+tDMA+tECC)
NERR = 118
RR2
> ECC capability CECC = 72
tDMA
In common cases, multiple (up to 25) retry steps occur
 Speculatively starts the next retry step
Speculative start

## Slide 18: Pipelined Read-Retry (PR2): Key Idea
tR
tECC
READ A
NERR = 232
tREAD
RR1
NERR = 173
RR(N – 1)
RRN
⋯
⋯
tRETRY’
NERR = 87
NERR = 23
= N×(tR+tDMA+tECC)
NERR = 118
RR2
= N×tR+tDMA+tECC
> ECC capability CECC = 72
tDMA
Removes tDMA & tECC
(~30% of each retry step) from the critical path
Latency
Reduction
Speculative start

## Slide 19: P&AR2: Outline
Read-Retry in Modern NAND Flash-Based SSDs
PR2: Pipelined Read-Retry
AR2: Adaptive Read-Retry
Evaluation Results

## Slide 20: Adaptive Read-Retry (AR2): Key Idea
tR
tECC
READ A
NERR = 232
tREAD
RR1
NERR = 173
RR(N – 1)
RRN
⋯
⋯
tRETRY
NERR = 87
NERR = 23
= N×tR+tDMA+tECC
NERR = 118
RR2
> ECC capability CECC = 72
tDMA

## Slide 21: Adaptive Read-Retry (AR2): Key Idea
tR
tECC
READ A
NERR = 232
tREAD
RR1
NERR = 173
RR(N – 1)
⋯
⋯
tRETRY
NERR = 87
= N×tR+tDMA+tECC
NERR = 118
RR2
tDMA
RRN
NERR = 23
> ECC capability CECC = 72
A large ECC margin
in the final retry step when read-retry succeeds
 Can we leverage this ECC (reliability) margin?

## Slide 22: Adaptive Read-Retry (AR2): Key Idea
tR
tECC
READ A
NERR = 232
tREAD
RR1
NERR = 173
RR(N – 1)
⋯
⋯
tRETRY
NERR = 87
= N×tR+tDMA+tECC
NERR = 118
RR2
tDMA
RRN
NERR = 23
> ECC capability CECC = 72
Trading the large ECC margin to reduce tR
tR’ = α×tR
+ e1
+ eN-1
+ e2
+ eN

## Slide 23: Adaptive Read-Retry (AR2): Key Idea
tR
tECC
READ A
NERR = 232
tREAD
RR1
NERR = 173
RR(N – 1)
⋯
⋯
tRETRY’
NERR = 87
= N×tR+tDMA+tECC
NERR = 118
RR2
tDMA
RRN
NERR = 23
> ECC capability CECC = 72
Trading the large ECC margin to reduce tR
tR’ = α×tR
+ e1
+ eN-1
+ e2
+ eN
 Further reduction in the read-retry latency
= N×α×tR+tDMA+tECC
Latency
Reduction

## Slide 24: Adaptive Read-Retry (AR2): Key Idea
tR
tECC
READ A
NERR = 232
tREAD
RR1
NERR = 173
RR(N – 1)
⋯
⋯
tRETRY’
NERR = 87
= N×tR+tDMA+tECC
NERR = 118
RR2
tDMA
RRN
AR2 reduces tR in every retry step
+ e1
+ eN-1
+ e2
= N×α×tR+tDMA+tECC
Latency
Reduction
NERR = 23
> ECC capability CECC = 72
+ eN
tR’ = α×tR

## Slide 25: Adaptive Read-Retry (AR2): Key Idea
tR
tECC
READ A
NERR = 232
tREAD
RR1
NERR = 173
RR(N – 1)
⋯
⋯
tRETRY’
NERR = 87
= N×tR+tDMA+tECC
NERR = 118
RR2
tDMA
RRN
AR2 reduces tR in every retry step
+ e1
+ eN-1
+ e2
= N×α×tR+tDMA+tECC
Latency
Reduction
tR’ = α×tR
NERR = 23
> ECC capability CECC = 72
+ eN
ensuring NERR < CECC in the final retry step

## Slide 26: Real-Device Characterization
160 real 48-layer TLC NAND flash chips
Observation 1: A large ECC margin in the final retry step even under worst-case operating conditions
  At most 40 errors per KiB under 1–year retention time @ 2K program and erase (P/E) cycles
  Use of near-optimal VREF in the final retry step
Observation 2: A large reliability margin incorporated in read-timing parameters
  25% tR reduction  At most 23 additional errors
  Worst-case-based design due to process variations
AR2 can easily work in commodity
NAND flash chips w/ at least 25% tR reduction

## Slide 27: P&AR2: Design
SSD Firmware (FTL)
P/E | tRET [days] | tR [μs]
< 250 | < 60 | 65
 | < 360 | 70
< 1.5K | < 60 | 70
 | < 360 | 75
Read–timing Parameter Table
(Pre-profiled)
⋯
⋯
⋯
⋯
⋯
⋯
⋯
Flash Controller
NAND Flash Chip
ECC Engine
READ A
READ A
Data A
Fail
tDMA
tECC
tR
ECC fail

## Slide 28: P&AR2: Design
SSD Firmware (FTL)
P/E | tRET [days] | tR [μs]
< 250 | < 60 | 65
 | < 360 | 70
< 1.5K | < 60 | 70
 | < 360 | 75
Read–timing Parameter Table
(Pre-profiled)
⋯
⋯
⋯
⋯
⋯
⋯
⋯
Flash Controller
NAND Flash Chip
ECC Engine
Fail
tDMA
tECC
tR
ECC fail
Best tR for the current operating conditions
Best tR
❶

## Slide 29: P&AR2: Design
SSD Firmware (FTL)
P/E | tRET [days] | tR [μs]
< 250 | < 60 | 65
 | < 360 | 70
< 1.5K | < 60 | 70
 | < 360 | 75
Read–timing Parameter Table
(Pre-profiled)
⋯
⋯
⋯
⋯
⋯
⋯
⋯
Flash Controller
NAND Flash Chip
ECC Engine
tDMA
tECC
tR
ECC fail
Best tR for the current operating conditions
Best tR
❶
Read-retry w/ best tR + speculative start
❷
Best tR
⋯
ECC success
Page A

## Slide 30: P&AR2: Design
SSD Firmware (FTL)
PEC | tRET [days] | tR [μs]
< 250 | < 60 | 65
 | < 360 | 70
< 1.5K | < 60 | 70
 | < 360 | 75
Read–timing Parameter Table
(Pre-profiled)
⋯
⋯
⋯
⋯
⋯
⋯
⋯
Flash Controller
NAND Flash Chip
ECC Engine
tDMA
tECC
tR
ECC fail
Best tR for the current operating conditions
Best tR
❶
Read-retry w/ best tR + speculative start
❷
Best tR
⋯
ECC success
Page A
Key Takeaway
Strong ECC: to avoid read-retry as much as possible
 Can provide high reliability margin
when read-retry occurs
 Can be used to reduce the read-retry latency

## Slide 31: P&AR2: Outline
Read-Retry in Modern NAND Flash-Based SSDs
PR2: Pipelined Read-Retry
AR2: Adaptive Read-Retry
Evaluation Results

## Slide 32: Evaluation Results
Simulation using MQSim [Tavakkol+, FAST18] and 12 real-world workloads
Our proposal improves SSD response time by
    Up to 51% (35% on average) compared to a high-end SSD w/o read-retry mitigation
    Up to 32% (17% on average) compared to a state-of-the-art read-retry mitigation technique [Shim+, MICRO19]

## Slide 33: P&S Modern SSDs Cutting-Edge Research in SSDs
Dr. Jisung Park
Prof. Onur Mutlu
ETH Zürich
Fall 2022
04 January 2023